VERY Important notice.

Don’t get too excited. Ford turbo setup is problematic that's why you bought this. So read and follow instructions below. Your excitement will be shortly lifted if you don’t, and we won’t warranty for your repairs.

The turbocharger’s oil inline filter (circled below) must be removed (not replaced) inside that male male fitting which connects to the banjo fitting of the factory oil pressure sender and turbocharger’s oil feeding line. It is located on the passenger side of the vehicle bolted on to the engine block. You will find it by tracing the factory turbocharger’s oil feeding line. IF YOU CAN NOT FIND IT, CALL US We are happy to remove this filter for you free of charge if you are unsure of how it should be removed. If installation occur at a workshop, Makes sure you ask workshop staff to keep and show you this filter before taking the car.

The oil feeding line must be replaced with a proper unrestrictive dash 4 size oil feeding line. Stock oil line is usually blocked with grease resulted from the blockage of the micro filter above. We can supply the oil feeding line for $150 AUD.

All fittings goes to the turbocharger must be cleaned and free from any dirt or flow restrictions. Note: Many Ebay oil feeding lines has built in restrictor in their fittings. Any oil restrictors must be drilled out to 4mms. Any oil feeding lines with a built in filter must have filter screen removed.

With engine filled to normal oil level before the old turbocharger is removed, with filter mentioned above removed and braided oil line fitted. Place turbocharger end’s oil feeding line’s banjo into a clean bottle, crank and start the car for 3 seconds, making sure there are plenty of clean oil coming out, oil flow must be like a open tap. The flow rate should be approximately 70ml/sec. After successful completion of this test, pour engine oil inside bottle back into the engine and start installation of the new turbocharger.

Before attach the oil drain pipe back onto the sump, crank start the car for 3 seconds and measure how much oil that comes out of the drain pip. You should have a flow rate similar to an open tab measuring close to 50mm/sec, not dripping. Once this test is completed successfully, secure the drain pipe. Silicon glue must not be used on any parts of the installation.

Turbo failure caused from oil related and foreign objects are excluded from our warranty.

Do contact us if you have any question relating to the installation of this turbocharger. Ph: 0413457185 / 03 90163965